Control and forwarding plane separation
on an open-source router
Linux Kongress
2010-09-23 in Nürnberg
Robert Olsson, Uppsala University
Olof Hagsand, KTH

---
 More than 10 year in production
at Uppsala University
ISP/SUNET
  AS1653
Full Internet routing
via EBGP/IBGP
2 * XEON 5630
TYAN 7025
4 *10g ixgbe sfp+ LR/SR
AS 2834
IPv4/IPv6
Local BGP peering
In Uppsala
OSPF
DMZ
Now at 10g towards ISP, SFP+ 850 nm, 1310nm
Stockholm
Stockholm
UU- 1
UU- 2
Interneral
UU-Net
L- green
L- red

---
Motivation
- Separate control-plane from forwarding plane
  A la IETF FORCES
- Control-plane: sshd, bgp, stats, etc on CPU core 0
- Forwarding-plane: Bulk forwarding on core1,..,coreN
- This leads to robustness of service against overload and DOS attacks, etc
- Enabled by:
  multi-core CPUs
  NIC hw classifiers
  Fast Buses (QPI/PCI-E gen2)

---
Control-plane separation on a multi-core
Control-Element
CE (core0)
Control traffic
FE1(core1)
Incoming traffic
Outgoing traffic
Classifier
FE2(core2)
Forwarding-Elements
Forwarding traffic
...
FEN(coreN)
Router

---
Hi-End Hardware
XEON 2 x E5630
TYAN S7025 Motherboard
Intel 82599

---
Block hardware structure
CPU0
Quad-core
CPU1
Quad-core
DDR3
DDR3
QPI
DDR3
DDR3
DDR3
DDR3
QPI
QPI
IOH
Tylersburg
IOH
Tylersburg
PCI-E Gen.2 x16
PCI-E Gen.2 x16
QPI
PCI-E Gen.2 x16
PCI-E Gen.2 x16
PCI-E Gen.2 x4
PCI-E Gen.2 x8
ESI
More I/O devices

---
Hi-End Hardware/Latency

---
Hardware - NIC
Intel 10g board Chipset 82599 with SFP+
Open chip specs. Thanks Intel!

---
Classification in the Intel 82599
The classification in the Intel 82599 consists of several steps, each is programmable.
This includes:
- RSS (Receiver-side scaling): hashing of headers and load-balancing
- N-tuples: explicit packet header matches
- Flow-director: implicit matching of individual flows.

---
Routing daemons
Packet forwarding is done in Linux kernel
Routing protocols is run in user-space
 daemons
Currently tested versions of quagga
Bgp, OSPF both IPv4, iPv6
Cisco API

---
Experiment 1:
flow separation external source
- Bulk forwarding data from source to sink (10Gb/s mixed packet lengths): mixed flow and packet lengths
- Netperf's TCP transactions emulated control data from a separate host
- Study latency of TCP transactions
Bulk data
TCP transactions
source
router
sink
host

---
N-tuple or Flowdirector
ethtool -K eth0 ntuple on
ethtool -U eth0 flow-type tcp4 src-ip 0x0a0a0a01 src-ip-mask
        0xFFFFFFFF dst-ip 0 dst-ip-mask 0 src-port 0 src-port-mask 0
        dst-port 0 dst-port-mask 0 vlan 0 vlan-mask 0 user-def 0
        user-def-mask 0 action 0
ethtool -u eth0
N-tuple is supported by SUN Niu and Intel ixgbe driver.
Actions are: 1) queue 2) drop
But we were lazy and patched ixgbe for ssh and BGP to use CPU0

---
N-tuple or Flowdirector
Even more lazy... we found the flow-director was implicitly programmed by outgoing flows. So both incoming and outgoing would use the same queue.
So if we set affinity for BGP, sshd etc we could avoid the N-tuple filters
 Example:
 taskset -c 0 /usr/bin/sshd
 Neat....

---
RSS is still using CPU0
So we both got our “selected traffic”
Plus the bulk traffic from RSS
We just want RSS to use “other” CPU's

---
Patching RSS
Just a one-liner...
diff --git a/drivers/net/ixgbe/ixgbe_main.c b/drivers/net/ixgbe/ixgbe_main.c
index 1b1419c..08bbd85 100644
--- a/drivers/net/ixgbe/ixgbe_main.c
+++ b/drivers/net/ixgbe/ixgbe_main.c
@@ -2379,10 +2379,10 @@ static void ixgbe_configure_rx(struct ixgbe_adapter *adapter)
        mrqc = ixgbe_setup_mrqc(adapter);
        if (adapter->flags & IXGBE_FLAG_RSS_ENABLED) {
- /* Fill out redirection table */
- for (i = 0, j = 0; i < 128; i++, j++) {
+ /* Fill out redirection table but skip index 0 */
+ for (i = 0, j = 1; i < 128; i++, j++) {
        if (j == adapter->ring_feature[RING_F_RSS].indices)
- j = 0;
+ j = 1;
        /* reta = 4-byte sliding window of
        * 0x00..(indices-1)(indices-1)00..etc. */
        reta = (reta << 8) | (j * 0x11);

---
Patching RSS
CPU- / core	0	1	2	3	4	5	6	7
Number / of packets	0	196830	200860	186922	191866	186876	190106	190412
No traffic to CPU core 0 still RSS gives fairness between other cores

---
Transaction Performance
netperf TCP_RR
On “router”
 taskset -c 0 netserver

---
Don't let forwarded packets
program the flowdirector
A new one-liner patch....
@@ -5555,6 +5555,11 @@ static void ixgbe_atr(struct ixgbe_adapter *adapter, struct sk_buff *skb,
        u32 src_ipv4_addr, dst_ipv4_addr;
        u8 l4type = 0;
+ if(!skb->sk) {
+ /* ignore nonlocal traffic */
+ return;
+ }
+
        /* check if we're UDP or TCP */
        if (iph->protocol == IPPROTO_TCP) {
        th = tcp_hdr(skb);

---
Instrumenting the flow-director
ethtool -S eth0 | grep fdir

---
Flow-director stats/1
     fdir_maxlen: 0
     fdir_maxhash: 0
     fdir_free: 8191
     fdir_coll: 0
     fdir_match: 195
     fdir_miss: 573632813 <--- Bulk forwarded data from RSS
     fdir_ustat_add: 1 <--- Old ssh session
     fdir_ustat_remove: 0
     fdir_fstat_add: 6
     fdir_fstat_remove: 0
     fdir_maxlen: 0
 ustat → user stats
 fstat → failed stats

---
Flow-director stats/2
        fdir_maxhash: 0
     fdir_free: 8190
     fdir_coll: 0
     fdir_match: 196
     fdir_miss: 630653401
     fdir_ustat_add: 2 <--- New ssh session
     fdir_ustat_remove: 0
     fdir_fstat_add: 6
     fdir_fstat_remove: 0

---
Flow-director stats/3
       fdir_maxlen: 0
     fdir_maxhash: 0
     fdir_free: 8190
     fdir_coll: 0
     fdir_match: 206 <--- ssh packets are matched
     fdir_miss: 645067311
     fdir_ustat_add: 2
     fdir_ustat_remove: 0
     fdir_fstat_add: 6
     fdir_fstat_remove: 0

---
Flow-director stats/4
     fdir_maxlen: 0
     fdir_maxhash: 0
     fdir_free: 32768 <-- Now incresed 32k
     fdir_coll: 0
     fdir_match: 0
     fdir_miss: 196502463
     fdir_ustat_add: 0
     fdir_ustat_remove: 0
     fdir_fstat_add: 0
     fdir_fstat_remove: 0

---
Flow-director stats/5
     fdir_maxlen: 0
     fdir_maxhash: 0
     fdir_free: 32764
     fdir_coll: 0
     fdir_match: 948 <-- netperf TCP_RR
     fdir_miss: 529004675
     fdir_ustat_add: 4
     fdir_ustat_remove: 0
     fdir_fstat_add: 44
     fdir_fstat_remove: 0

---
Transaction latency using flow separation

---
Experiment 1 results
- Baseline (no background traffic) gives 30000 transactions per second
- With background traffic using RSS over all cores gives increase in transaction latency reducing transactions per second to ~5000
- The RSS patch (dont forward traffic on core 0) brings the transaction latency back to (almost) the same case as the baseline
- In all cases the control traffic is bound to core 0

---
Experiment 2:
Flow separation in-line traffic
- Inline control within bulk data (on same incoming interface)
- Study latency of TCP transactions
- Work in progress
TCP transactions
Bulk data
source
router
sink

---
Results in-line
Transaction latency wo/w RSS path
Flow mix and 64 byte packets
Zoom in of 64 byte packets

---
Classifier small packet problem
Seems we drop a lot packets before they are classified
DCB (Data Center Bridging) has a lot of
features to prioritize different type of traffic.
But only for IEEE 802.1Q
VMDq2 suggested by Peter Waskiewicz Jr
at Intel

---
Experiment 3:
Transmit limits
Investigate hardware limits by transmitting as much as possible from all cores simultaneously.
CPU0
Quad-core
CPU1
Quad-core
DDR3
DDR3
QPI
DDR3
DDR3
DDR3
DDR3
QPI
QPI
IOH
Tylersburg
IOH
Tylersburg
PCI-E Gen.2 x16
PCI-E Gen.2 x16
QPI
PCI-E Gen.2 x16
PCI-E Gen.2 x16
PCI-E Gen.2 x4
PCI-E Gen.2 x8
ESI
More I/O devices

---
pktgen/setup
Inter-face	eth0	eth1	eth2	eth3	eth4	eth5	eth6	eth7	eth8	eth9
CPU-core	0	1	2	3	4	5	6	7	12	13
Mem / node	0	0	0	0	1	1	1	1	1	1
 eth4, eth5 on x4 slot

---
Setup
CPU0
Quad-core
CPU1
Quad-core
Memory node 0
Memory node1
QPI
QPI
QPI
eth0
IOH
Tylersburg
IOH
Tylersburg
eth6
eth1
QPI
eth7
eth2
eth8
eth3
eth9
eth4
eth5

---
TX w. 10 * 10g ports
93Gb/s “Optimal”

---
Conclusions
- We have shown traffic separation in a high-end multi-core PC with classifier NICs by assigning one CPU core as control and the other as forwarding cores. Our method:
  - Interrupt affinity to bind control traffic to core 0
  - Modified RSS to spread forwarding traffic over all except core 0
  - Modified the flow-director implementation slightly by only
   letting local (control) traffic populate the flowdir table.
- There are remaining issues with packet drops in in-line separation
- We have shown 93Gb/s simplex transmission bandwidth on a fully equipped PC platform

---
That's all
Questions?

---
Rwanda example

---
Lagos next

---
Low-Power Development
Some ideas
Power consumption
SuperMicro X7SPA @ 16.5 Volt with picoPSU
Watt Test
-------------------
1.98 Power-Off
13.53 Idle
14.35 1 core
15.51 2 Core
15.84 3 Core
16.50 4 Core
Routing Performance about 500.000 packet/sec in optimal setup.

---
Example herjulf.se
14 Watt by 55Ah battery
bifrost/USB + lowpower disk

---
Running on battery

---
SuperCapacitors

---
DOM - Optical Monitoring
Optical modules can support optical link monitoring
RX, TX power, temperatuers, alarms etc
Newly added support to Bifrost/Linux

---
DOM
ethtool -D eth3
Int-Calbr: Avr RX-Power: RATE_SELECT: Wavelength: 1310 nm
        Temp: 25.5 C
        Vcc: 3.28 V
        Tx-Bias: 20.5 mA
        TX-pwr: -3.4 dBm ( 0.46 mW)
        RX-pwr: -15.9 dBm ( 0.03 mW)