 Kernel/Hardware for bifrost
Linux for infrastructure
  - Robustness, robustness, performance
  - No chance to support all HW or SW
  - Selection in lab
  - Very time consuming process
    - Costly, need resources and needs support & skill

---
We still on use Opteron
  - Now Shanghai 2382 or close
  - Motherboard TYAN 2915, 2923, two NUMA nodes
  - Memory config to reach 128 bit transfers
  - Chassies, redundant power
  - USB boot seems OK.
  - No recommendations for low or mid range HW!!

---
NIC's (Recommended)
  - 10g Intel 82598 chips fixed 10GBASE-SR
  - SUN neptune 10g/1g, XFP modules
  - Intel 82576. GIGE. TP
  - XFP-LR can drive fibre 40km or more
    - Tested at KTH/CSD
  - 10GBASE-T not seen yet
  - Hot-Lava SFP board?

---
Drivers
Critical. Drivers and Kernel support
  - Almost critital. Open chip documentation
  - Multiqueue. RSS a la MS NDIS 6.0 and later
  - Ixgbe, niu, igb (e1000, e1000e, tulip)
  - Issues: Optical Statistics, DOM etc

---
Kernel selection
Long time monitor and test. Code Freeze.
Now 2.6.29-rc2 from DaveM git with many pathes
do {
   modify_and_patch();
   happy = test();
} while( ! happy);

---
Multiqueue efforts landed.
  - Needs: NIC, Driver, Affinity, Understanding
Linux Network framework for MO
Thanks, DaveM
eth-affinity
cat /proc/interrups
    IRQ/DMA consistant naming
driver patches.
       ixgbe, niu, igb

---
Multiqueue efforts landed.
  - HW classifier splits incoming based on hash etc	to	different MSI-X IRQ vectors (For RX)
  - We set IRQ affinity so:
    - RXQ1 → CPU1
    - RXQ2 → CPU2 etc. This done automaticly by eth-affinity it can be done due the consistent naming in /proc/interrupts

---
Multiqueue efforts landed.
  - At RX the driver records the RX queue in the skb
@@ -3815,6 +3824,8 @@ static void igb_receive_skb(struct igb_ring *ring, u8 status,
        struct igb_adapter * adapter = ring->adapter;
        bool vlan_extracted = (adapter->vlgrp && (status & E1000_RXD_STAT_VP));
+ skb_record_rx_queue(skb, rp->rx_channel);
+

---
Multiqueue efforts landed.
  - At TX the driver selects the TX queue according to RX
+static u16 select_queue(struct net_device *dev, struct sk_buff *skb)
+{
+ if( dev->real_num_tx_queues && skb_rx_queue_recorded(skb) )
+ return skb_get_rx_queue(skb) % dev->real_num_tx_queues;
+
+ return smp_processor_id() % dev->real_num_tx_queues;
+}
+

---
Multiqueue efforts landed
Of course we have also set IRQ affinity so:
TXQ1 → CPU1
TXQ2 → CPU2 etc. This done automaticly by eth-affinity it can be done due the consistent naming in /proc/interrupts

---
Multiqueue efforts landed
This OK for fowarding...
Packets Per Sec scales with No CPU Cores
Detailed numbers in the IIS report
Ixia measued roughly 2.8Mpps Duplex 3.5 Mpps simplex.
8.6 Gbits/s (1.8 Mpps) with Internet traffic load with simplex forwarding.

---
Known issues
  - Intel new 82599 chip not supported.
  - quagga netlink. 32 vs 64 bit kernel
    - Do we need quagga for 64 bit? No real problem

---
New directions for development & research?
Explore advanced classifier benefits
  - Control Plane, Route w/o dst cache etc?
Energy
  - Low-Power routing and networking

---
 Time for Questions!