Towards 10Gb/s open-source routing
Olof Hagsand (KTH)
Robert Olsson (Uppsala U)
Bengt Görden (KTH)
Linuxkongress 2008

---
Introduction
Investigate packet forwarding performance of new PC hardware:
  - Multi-core CPUs
  - Multiple PCI-e buses
  - 10G NICs
Can we obtain enough performance to use open-source routing also in the 10Gb/s realm?

---
Measuring throughput
Packet per second
  - Per-packet costs
  - CPU processing, I/O and memory latency, clock frequency
Bandwidth
  - Per-byte costs
  - Bandwidth limitations of bus and memory

---
Measuring throughput
drops
breakpoint
capacity
overload
overload

---
Router Evolution, 3rd Generation
Inside a router, HW style
Switched backplane
CPU Card
Multiple simultaneous transfers over the backplane
Specialized hardware: ASICs, NPUs, backplane with switching stages or crossbars
Line Card
Buffer
Memory
forwarder
Line Card
Buffer
Memory
forwarder
Line Card
Buffer
Memory
forwarder
Line Card
Buffer
Memory
forwarder
CPU
RIB

---
Inside a router, PC-style
Shared bus backplane
Line
Card
Line
Card
Every packet goes twice over shared bus to the CPU
Cheap, but low performance
But lets increase the # of CPUs and # of buses!
Line
Card
Buffer
Memory
CPU
RIB

---
Block hw structure

---
Hardware – Box (set 2)
AMD Opteron 2356 with one quad core 2.3GHz Barcelona
CPUs on a TYAN 2927 Motherboard (2U)

---
Hardware - NIC
Intel 10g board Chipset 82598
Open chip specs. Thanks Intel!

---
Lab

---
Equipment summary
Hardware needs to be carefully selected
BifrostLinux on kernel 2.6.24rc7 with LC-trie forwarding
Tweaked pktgen
Set 1: AMD Opteron 2222 with two double core 3GHz CPUs on a Tyan Thunder n6650W(S2915) motherboard
Set 2: AMD Opteron 2356 with one quad core 2.3GHz Barcelona CPUs on a TYAN 2927 Motherboard (2U)
Dual PCIe buses
10GE network interface cards.
  - PCI Express x8 lanes based on Intel 82598 chipset

---
Experiments
Transmission(TX)
  - A bandwidth of 25.8 Gb/s and a packet rate of 10 Mp/s using four CPU cores and two PCIe buses
Forwarding experiments
  - Single IP flow was forwarded using a single CPU.
  - Realistic multiple-flow stream with varying destination address and packet sizes using a single CPU.
  - Multi-queues on the interface cards were used to dispatch different flows to four different CPUs.

---
Tx Experiments
Goal:
  - Just to see how much the hw can handle – upper limit
Loopback tests over fibers
Don't process RX packets just let MAC count them
These numbers can give indication what forwarding capacity is possible
Experiments:
  - Single CPU TX single interface
  - Four CPUs TX one interface each
Tested device

---
Tx single sender: Packets per second

---
Tx single sender: Bandwidth

---
Tx - Four CPUs: Bandwidth
CPU 1
CPU 2
CPU 3
CPU 4
SUM
Packet length: 1500 bytes

---
TX Experiments summary
Single Tx sender is primarily limited by PPS at around 3.5Mpps
A bandwidth of 25.8 Gb/s and a packet rate of 10 Mp/s using four CPU cores and two PCIe buses
This shows that the hw itself allows 10Gb/s performance
We also see nice symmetric Tx between the CPU cores.

---
Forwarding experiments
Goal:
  - Realistic forwarding performance
Overload ,measurements (
Single forwarding path from one traffic source to one traffic sink
  - Single IP flow was forwarded using a single CPU.
  - Realistic multiple-flow stream with varying destination address and packet sizes using a single CPU.
  - Multi-queues on the interface cards were used to dispatch different flows to four different CPUs.
Test Generator
Tested device
Sink device

---
Single flow, single CPU: Packets per second

---
Single flow, single CPU: Bandwidth

---
Single sender forwarding summary
Virtually wire-speed for 1500-byte packets
Little difference between forwarding on same card, different ports, or between different cards
  - Seems to be slightly better perf on same card, but not significant
Primary limiting factor is pps, around 900Kpps
TX has small effect on overall performance

---
Introducing realistic traffic
For the rest of the experiments we introduce a more realistic traffic scenario
Multiple packet sizes
  - Simple model based on realistic packet distribution data
Multiple flows (multiple dst IP:s)
  - This is also necessary for multi-core experiments since NIC classification is made using hash algorithm on packet headers

---
Packet size distribution
Real data from www.caida.org, Wide aug 2008

---
Flow distribution
Flows have size and duration distributions
8000 simultaneous flows
Each flow 30 packets long
  - Mean flow duration is 258 ms
31000 new flows per second
  - Measured by dst cache misses
Destinations spread randomly over 11.0.0.0/8
FIB contains ~ 280K entries
  - 64K entries in 11.0.0.0/8
This flow distribution is relatively aggressive

---
Multi-flow and single-CPU: PPS & BW
max
min
Set 1
Set 1
Set 2
Set 2
Small routing table	280K entries
No ipfilters	ipfilters enabled

---
Multi-Q experiments
Use more CPU cores to handle forwarding
NIC classification (Receiver Side Scaling RSS) uses hash algorithm to select input queue
Allocate several interrupt channels, one for each CPU.
Flows are distributed evenly between CPUs
  - need agregated traffic with multiple flows
Questions:
  - Are flows evenly distributed?
  - Will performance increase as CPUs are added?

---
Multi-flow and Multi-CPU (set 1)
1 CPU 4 CPUs CPU #1 CPU #2 CPU #3 CPU #4
Only 64 byte packets

---
Results MultiQ
Packets are evenly distributed between the four CPUs.
But forwarding using one CPU is better than using four CPUs!
Why is this?

---
Profiling.
Single CPU
Multiple CPUs
samples % symbol name
396100 14.8714 kfree
390230 14.6510 dev_kfree_skb_irq
300715 11.2902 skb_release_data
156310 5.8686 eth_type_trans
142188 5.3384 ip_rcv
106848 4.0116 __alloc_skb
75677 2.8413 raise_softirq_irqoff
69924 2.6253 nf_hook_slow
69547 2.6111 kmem_cache_free
68244 2.5622 netif_receive_skb
samples % symbol name
1087576 22.0815 dev_queue_xmit
651777 13.2333 __qdisc_run
234205 4.7552 eth_type_trans
204177 4.1455 dev_kfree_skb_irq
174442 3.5418 kfree
158693 3.2220 netif_receive_skb
149875 3.0430 pfifo_fast_enqueue
116842 2.3723 ip_finish_output
114529 2.3253 __netdev_alloc_skb
110495 2.2434 cache_alloc_refill

---
Multi-Q analysis
With multiple CPUs: TX processing is using a large part of the CPU making using more CPUs sub-optimal
It turns out that the Tx and Qdisc code needs to be adapted to scale up performance

---
MultiQ: Updated drivers
We recently made new measurements (not in paper) using updated driver code
We also used hw set 2 (Barcelona) to get better results
We now see an actual improvement when we add one processor
(More to come)

---
Multi-flow and Multi-CPU (set 2)
1 CPU 2 CPUs 4 CPUs

---
Conclusions
Tx and forwarding results towards 10Gb/s performance using Linux and selected hardware
>25Gb/s Tx performance
Near 10Gb/s wirespeed forwarding for large packets
Identified bottleneck for multi-q and multi-core forwarding.
If this is removed, upscaling performance using several CPU cores is possible to 10Gb/s and beyond.